## Slide 1: The Processor

## Slide 2: What is a processor?
A processor has some state:
  uint32 r[32]; // thirty two registers
  uint32 imem[4096]; // 16KB of instruction memory
  uint32 dmem[4096]; // 16KB of data memory
  uint32 pc; // the program counter (next instruction to be executed)
A processor understands a certain number of “commands”
  These are called the processor instruction set
  Instructions perform transformations on the state
    Add two registers, write to dmem, etc…
A processor’s job is to execute a (never ending) sequence of instructions
  Until powered off
An Instruction Set Architecture (ISA) is the precise definition of
  processor state + instruction set + operating rules

## Slide 3: Processor “algorithm”
uint32 r[32]; // thirty two registers
uint32 imem[4096]; // 16KB of instruction memory
uint32 dmem[4096]; // 16KB of data memory
uint32 pc; // the program counter (next instruction to be executed)
pc = initial_val;
while ( 1 )
{
  uint32 instruction = imem[pc];
  if ( instruction == … ) { do something }
  else if ( instruction == … ) { do something else }
  else { panic(“i don’t know this instruction”); }
  pc = (pc + 1) % 4096;
}

## Slide 4: Let’s define some instructions
We want to add two of our registers and put the result in a register
  add r[1], r[7]  r[5]
We want to read some data from “dmem” and put it in a register
  load dmem[r[6]]  r[11]
We want to store the value of a register into dmem
  store r[2]  dmem[r[6]]
We need to think how we encode these different instructions in 32b
In a way that’s easy to then know what the instruction does…

## Slide 5: Let’s encode our instructions (1)
add r[1], r[7]  r[31]
  Need to encode the operation: “add”  00 -- how many bits???
  Need to encode the first register: ra  00001 -- 5 bits for 32 regs
  Need to encode the second register: rb  00111 -- 5 bits for 32 regs
  Need to encode the dest register: rd  11111 -- 5 bits for 32 regs
  Total 15 + a few bits for the operation
lw dmem[r[6]]  r[11]
  Need to encode the operation: “lw”  01 -- how many bits???
  Need to encode the first register: ra  00110 -- 5 bits for 32 regs
  Need to encode the second register: rb  xxxxxx -- 5 bits for 32 regs
  Need to encode the dest register: rd  01011 -- 5 bits for 32 regs
  Total 10 + a few bits for the operation
sw r[2]  dmem[r[6]]
  Need to encode the operation: “sw”  10 -- how many bits???
  Need to encode the first register: ra  00010 -- 5 bits for 32 regs
  Need to encode the second register: rb  00110 -- 5 bits for 32 regs
  Need to encode the dest register: rd  xxxxxx -- 5 bits for 32 regs
  Total 10 + a few bits for the operation

## Slide 6: Let’s encode our instructions (2)
Well, we’ll need more operations than just “add”, right?
Let’s pick a list of operations we want to support, and give them an encoding:
Operation | Encoding
Add | 0000
Lw | 0001
Sw | 0010
Sub | 0011
Mul | 0100
Div | 0101
And | 0110
Or | 0111
Operation | Encoding
Xor | 1000
 | 1001
 | 1010
 | 1011
 | 1100
 | 1101
 | 1110
 | 1111

## Slide 7: Let’s encode our instructions (3)
We need to pick which bits indicate what in an instruction
Opcode
3--0
Ra
18--14
Rb
13--9
Rd
8-4
Free
31--19
add ra, rb  rd
Opcode
3--0
Rb
13--9
Rd
8-4
Free
31--14
lw dmem[rb]  rd
sub ra, rb  rd
mul ra, rb  rd
div ra, rb  rd
and ra, rb  rd
or ra, rb  rd
xor ra, rb  rd
Opcode
3--0
Rb
13--9
Rd
8-4
Free
31--14
sw rd  dmem[rb]

## Slide 8: Let’s add the instructions to the processor
pc = initial_val;
while ( 1 )
{
  uint32 instruction = imem[pc];
  uint32 opcode = instruction & 0xf;
  uint32 ra = (instruction >> 14) & 0x1f;
  uint32 rb = (instruction >> 9) & 0x1f;
  uint32 rd = (instruction >> 4) & 0x1f;
  if ( opcode == 0x0 ) { r[rd] = r[ra] + r[rb]; ) // ADD
  else if ( opcode == 0x1 ) { r[rd] = dmem[r[rb]]; ) // LW
  else if ( opcode == 0x2 ) { dmem[r[rb]] = r[rd]; ) // SW
  else { panic(“i don’t know this instruction”); }
  pc = (pc + 1)%4096;
}

## Slide 9: Let’s write a program for our processor
Let’s divide two integers a, b, and produce the division and reminder
  The “a” value is located at address 0x100
  The “b” value is located at address 0x200
  We want the quotient (a/b) stored to address 0x300
  We want the reminder (a rem b) stored to address 0x400
Algorithm
  q = 0;
  while ( a >= b ) { q++; a = a-b; }
  r = a;

## Slide 10: How do we implement a loop? Branches!
Add some instructions that changes the PC register
  If done unconditionally, this is called a jump
  If done conditionally, this is called a branch
beq ra, rb, offset  if ( r[ra] == r[rb] ) pc = pc + offset
bge ra, rb, offset  if ( r[ra] >= r[rb] ) pc = pc + offset
bgt ra, rb, offset  if ( r[ra] > r[rb] ) pc = pc + offset
jump ra  pc = r[ra]
Opcode
3--0
Ra
18--14
Rb
13--9
OffsetLo
8-4
OffsetHi
31--19
beq ra, rb, offset
bgt ra, rb, offset
bge ra, rb, offset
Opcode
3--0
Ra
18--14
Free
13--9
Free
8-4
Free
31--19
Jump ra

## Slide 11: Let’s add branches to the processor algorithm
pc = initial_val;
while ( 1 )
{
  uint32 instruction = imem[pc];
  uint32 opcode = instruction & 0xf;
  uint32 ra = (instruction >> 14) & 0x1f;
  uint32 rb = (instruction >> 8) & 0x1f;
  uint32 rd = (instruction >> 4) & 0x1f;
  int32 offset = (((int32)instruction >> 18) & 0x1FFFF))<<5) || rd; // preserve sign
  Bool taken = 0;
  if ( opcode == 0x0 ) { r[rd] = r[ra] + r[rb]; } // ADD
  else if ( opcode == 0x1 ) { r[rd] = dmem[(r[rb] +offset) % 4096 ]; } // LW
  else if ( opcode == 0x2 ) { dmem[(r[rb] + offset)%4096 ] = r[rb]; } // SW
  else if ( opcode == 0x3 && r[ra] == r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BEQ
  else if ( opcode == 0x4 && r[ra] > r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGT
  else if ( opcode == 0x5 && r[ra] >= r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGE
  else if ( opcode == 0x6 ) { pc = (r[ra]) % 4096; taken = 1} // JUMP
  else { panic(“i don’t know this instruction”); }
  If ( taken == 0 ) pc = (pc + 1)%4096;
}

## Slide 12: One more detail… Loading constants…
How do we implement “q++”?
  We need to do q = q + 1
  Where do we get the number 1 from? Memory?
New instruction to load constants: “load immediate”
LI #<immediate>, r[rd]  r[rd] = <immediate>
How big is the immediate? It depends on the encoding
  23 bits available
  Note we can’t have a 32b value, which would be ideally what we want
  So…. Do we put the constant in the lower or the upper bits of the destination?
We need to decide what to do with the 9 bits missing
  Immediate = 7000a = 111_0000_0000_0000_1010
  Rd = xxxx_xxxx_x111_0000_0000_0000_1010
  What do we put in those “x” bits?
  Think how would you load the constant “-1”…..
Options: Zero Extend, Sign Extend
  Zero Extend: always put zeros
  Sign extend: take highest bit of the immediate and replicate across the 9 bits
Opcode
3--0
Rd
8-4
Immediate
31--9
Li #immediate -> r[rd]

## Slide 13: Load Immediate (constant into register)
pc = initial_val;
while ( 1 )
{
  uint32 instruction = imem[pc];
  uint32 opcode = instruction & 0xf;
  uint32 ra = (instruction >> 14) & 0x1f;
  uint32 rb = (instruction >> 8) & 0x1f;
  uint32 rd = (instruction >> 4) & 0x1f;
  int32 offset = (((int32)instruction >> 18) & 0x1FFFF))<<5) || rd; // preserve sign
  Int32 immediate = (int32)(instruction >> 9);
  if ( opcode == 0x0 ) { r[rd] = r[ra] + r[rb]; } // ADD
  else if ( opcode == 0x1 ) { r[rd] = dmem[(r[rb] +offset) % 4096 ]; } // LW
  else if ( opcode == 0x2 ) { dmem[(r[rb] + offset)%4096 ] = r[rb]; } // SW
  else if ( opcode == 0x3 && r[ra] == r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BEQ
  else if ( opcode == 0x4 && r[ra] > r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGT
  else if ( opcode == 0x5 && r[ra] >= r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGE
  else if ( opcode == 0x6 ) { pc = (r[ra]) % 4096; taken = 1} // JUMP
  else if ( opcode == 0x7 ) { r[rd] = sign_extend(immediate); } // LI
  else { panic(“i don’t know this instruction”); }
  If ( taken == 0 ) pc = (pc + 1)%4096;
}

## Slide 14: Let’s write a program for our processor
Let’s divide two integers a, b, and produce the division and reminder
  The “a” value is located at address 0x100
  The “b” value is located at address 0x200
  We want the quotient (a/b) stored to address 0x300
  We want the reminder (a rem b) stored to address 0x400
Algorithm
  q = 0;
  while ( a >= b ) { q++; a = a-b; }
  r = a;

## Slide 15: What about the “panic” thing?
pc = initial_val;
while ( 1 )
{
  uint32 instruction = imem[pc];
  uint32 opcode = instruction & 0xf;
  uint32 ra = (instruction >> 14) & 0x1f;
  uint32 rb = (instruction >> 8) & 0x1f;
  uint32 rd = (instruction >> 4) & 0x1f;
  int32 offset = (((int32)instruction >> 18) & 0x1FFFF))<<5) || rd; // preserve sign
  Int32 immediate = (int32)(instruction >> 9);
  if ( opcode == 0x0 ) { r[rd] = r[ra] + r[rb]; } // ADD
  else if ( opcode == 0x1 ) { r[rd] = dmem[(r[rb] +offset) % 4096 ]; } // LW
  else if ( opcode == 0x2 ) { dmem[(r[rb] + offset)%4096 ] = r[rb]; } // SW
  else if ( opcode == 0x3 && r[ra] == r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BEQ
  else if ( opcode == 0x4 && r[ra] > r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGT
  else if ( opcode == 0x5 && r[ra] >= r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGE
  else if ( opcode == 0x6 ) { pc = (r[ra]) % 4096; taken = 1} // JUMP
  else if ( opcode == 0x7 ) { r[rd] = sign_extend(immediate); } // LI
  else { panic(“i don’t know this instruction”); }
  If ( taken == 0 ) pc = (pc + 1)%4096;
}

## Slide 16: What about the “panic” thing?
pc = initial_val;
while ( 1 )
{
  uint32 instruction = imem[pc];
  uint32 opcode = instruction & 0xf;
  uint32 ra = (instruction >> 14) & 0x1f;
  uint32 rb = (instruction >> 8) & 0x1f;
  uint32 rd = (instruction >> 4) & 0x1f;
  int32 offset = (((int32)instruction >> 18) & 0x1FFFF))<<5) || rd; // preserve sign
  Int32 immediate = (int32)(instruction >> 9);
  if ( opcode == 0x0 ) { r[rd] = r[ra] + r[rb]; } // ADD
  else if ( opcode == 0x1 ) { r[rd] = dmem[(r[rb] +offset) % 4096 ]; } // LW
  else if ( opcode == 0x2 ) { dmem[(r[rb] + offset)%4096 ] = r[ra]; } // SW
  else if ( opcode == 0x3 && r[ra] == r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BEQ
  else if ( opcode == 0x4 && r[ra] > r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGT
  else if ( opcode == 0x5 && r[ra] >= r[rb] ) { pc = (pc + offset) % 4096; taken = 1} // BGE
  else if ( opcode == 0x6 ) { pc = (r[ra]) % 4096; taken = 1} // JUMP
  else if ( opcode == 0x7 ) { r[rd] = sign_extend(immediate); } // LI
  else { pc = 3090 } // Must be published in our ISA document for the OS to know
  If ( taken == 0 ) pc = (pc + 1)%4096;
}

## Slide 17
<pause>

## Slide 18: Let’s turn our processor into Hardware…

## Slide 19: Basic Gates
And, Or, Xor
Mux
The clock signal
Latch, Flop

## Slide 20: Idea: Draw Single-Cycle Machine with flops on the left
pc
r0
r1
r2
r31
imem
dmem
ctrl
alu

## Slide 21
PC32
Imem[0]
Imem[1]
Imem[4095]
dmem[0]
dmem[1]
dmem[4095]
r0
r1
r31
+
1
Clock
nextpc
pc
instruction
32
opcode
Bits 3:0
ra
rb
rd
Bits18:14
Bits 13:9
Bits 8:4
+,-
5
R[ra]
R[rb]
Mem[r[ra]]
Opcode[0:0]
0
1
offset
Bits 31-19
Is_zero
+